## Slide 1: Geothermal Project “ECOGI“ in Rittershoffen, France Clément Baujard Reservoir Engineer, ES-Geothermie

## Slide 2: ES Group: main activities
ES Group belongs to EDF at 88%
Staff 1200, 2014 turnover 945 M€
1st energy supplier in Alsace (Eastern France)
ES Géothermie (ESG), 100% subsidiary ES

## Slide 3: ES-Geothermie: who are we?
SME 23 employees
Turnover : 2Mio €

## Slide 4: ES-Geothermie: what do we do?
General contracting for deep geothermal projects, from exploration to power plant commissioning - Permitting, Feasibility studies, Design and detailed planning, tendering process and specifications, selection of subcontractors, management, coordination and works supervision, reporting (…)
Power Plant operation - Soultz-sous-forêts and Rittershoffen
Consulting activities and services - Planning and interpretation of well logs, Reservoir engineering and development strategy, Platform design and realization, Pump and power plant design, Interpretation of geophysical data, 3D geological modelling, Well targeting and trajectory, Real-time seismic monitoring, Design, planning, realization and interpretation of pumping tests, Handling of natural radioactivity issues, Database handling for well data, Communication (…)
Hardware - Seismic Monitoring stations, Tubes/Connections/Production test wellhead assembly and lines, PTQ Sensors for surface monitoring and acquisition module, Secured data servers, Pumps, tanks, separators, (…)
Software - SLB Petrel, Wellcad, Autocad, Seiscomp, AQTESolv, Surfer, Matlab, (…)
Research activities - Chair in Strasbourg University, H2020 projects (…)

## Slide 5: ES-Geothermie consulting and services
EGS Services
Seismic exploration
2D geology & 3D model
Sismological station network
Induced microseismic monitoring
Reservoir logging & testing
Surface facilities
Environment
& Acceptability

## Slide 6: Alsace (« Elzass ») Geothermal context
Temperature data from Liag
Hurtig et al, 1992
Several large-scale thermal anomalies in Europe
Tertiary grabens (Upper Rhine Valley) with many geothermal projects
Temperature range > 150°C

## Slide 7: Soultz / Rittershoffen temperature anomaly
Temperature distribution within the URG at 1500 m depth (LIAG)
ECOGI
Baillieux, 2012
Fault map and temperature field
between Soultz and Rittershoffen
Stockstadt
Wattenheim
Speyer
Landau
Soultz
Strasbourg
Sélestat

## Slide 8: Geothermal exploitation in URG
Soultz
Rittershoffen
Landau
Insheim
Bruchsal
Landau
Combined Heat & Power plant
3MWe+ district heating
Soultz 2.2MWe
Insheim 4.8MWe
Rittershoffen

## Slide 9: Upper Rhine Graben cross-section
Soultz
Rhine
Top basement
1400 m
Top basement
> 5500 m
Top basement
2200 m
Rittershoffen
Soultz : fractured sandstone

## Slide 10: Hydro-thermal conceptual model
°C
Pechelbronn
Soultz
Baden-Baden
SE
NW
10
225
0
10
20
30
40
50
60
70
km
6
4
2
0
Rhin
Rittershoffen
From Le Carlier et al., 1994

## Slide 11: ECOGI Project: overview
ECOGI: Exploitation de la Chaleur d’Origine Géothermale pour l’Industrie
Located in Rittershoffen, France
Joint venture: ES (40%), Roquette Frères (40%), Caisses dépôts (20%)
55 M€ total investment
25 M€ French incentive from Fonds Chaleur
Geothermal project: 25MWth over 100MWth
Beinheim Biorefinery
Notes: Fabrice Gourdellier

## Slide 12: ECOGI Project: overview
Construction of a geothermal station (Rittershoffen), a heat transport and exploitation loop destined to supply overheated hot water to the industrial facility of Roquette Frères in Beinheim

## Slide 13: ECOGI Project: main technical phases
2011 |  | 2012 |  | 2013 |  | 2014 |  | 2015 |  | 2016 | 
ECOGI |  |  |  |  |  |  |  |  |  |  | 
JV creation |  |  |  |  |  |  |  |  |  |  | 
 | Drilling |  |  |  |  |  |  |  |  |  | 
 | Platform construction |  |  |  |  |  |  |  |  |  | 
 |  |  | GRT1 |  |  |  |  |  |  |  | 
 |  |  | Drilling and well development |  |  |  |  |  |  |  | 
 |  |  |  |  | Seismic |  |  |  |  |  | 
 |  |  |  |  | Survey |  |  |  |  |  | 
 |  |  |  |  |  | GRT2 |  |  |  |  | 
 |  |  |  |  |  | Drilling and tracer tests |  |  |  |  | 
 |  |  |  |  |  |  |  | Surface loop |  |  | 
 |  |  |  |  |  |  |  | Thermal plant |  |  | 
 |  |  |  |  |  |  |  | Thermal loop |  |  | 
 |  |  |  |  |  |  |  | Bio-reffinery |  |  | 
 |  |  |  |  |  |  |  |  |  | ECOGI | 
 |  |  |  |  |  |  |  |  |  | Commissioning | 
© ECOGI

## Slide 14: Geothermal and geological context
Offset wells
Oil exploration wells from the 80’s
Soultz-sous-Forêts geothermal wells
Seismic data
Vintage seismic lines from the 80’s
2 seismic profiles in the framework of the project
-> Thermal anomaly
-> Regional fault zone

## Slide 15: Well targets
GRT-1 (vertical): 2600m MD
GRT-2 (deviated): 3200m MD
Both wells target the fault zone in the basement

## Slide 16: GRT-1: drilling and completion
Rig: Cofor Entrepose drilling MAS 8000
Drilled in 2012
Duration: 3 months

## Slide 17: GRT-1 Well testing and development strategy
GRT-1 Well development
Thermal stimulation
Chemical stimulation
Hydraulic stimulation
Well testing GRT-1
Low initial productivity (< 0,5L/s/bar), high skin (20)
Low initial injectivity
Economic threshold not reached

## Slide 18: GRT-1 Thermal stimulation
Low rate and low pressure cold water injection during 3 days
Objective: cool-down the rock matrix and increase natural fractures aperture
Results:
Injectivity increase (1,5x)
low seismological activity

## Slide 19: GRT-1 Chemical stimulation
Specially designed green acids were injected (glutamate based)
Focused, low volume injections using coiled tubing and OH-packers (3 intervals selected based on cutting and wellbore imaging data)
Objective: clean fracture fillings
Results: Injectivity increase (1,5x)

## Slide 20: GRT-1 Hydraulic stimulation
Results: Injectivity increase (2x)
High rate water injection
Step-rate injections
Real-time seismological monitoring
Objective: increase reservoir permeability using hydro-shear processes

## Slide 21: Seismic monitoring network

## Slide 22: Induced seismicity during GRT-1 hydraulic stimulation
Critical threshold (Ml 1,7) never reached
Real-time location
More than 300 events automatically picked and located
Max magnitude 1,6 Ml
  Maurer et al 2016

## Slide 23: GRT-1 well development results
GRT-1 Injectivity x 5
Decision to drill GRT-2

## Slide 24: Exploration (2D seismic) after GRT-1
2x 2D seismic lines were shot after drilling GRT-1
1 VSP
Objective: secure GRT-2 target

## Slide 25: 2D Seismic profiles [time]

## Slide 26: 2D seismic profiles interpretation [time]

## Slide 27: Interpretation + GRT-1 [time + z]

## Slide 28: Interpretation + GRT-1 [time + z]]

## Slide 29: GRT-2: drilling and completion
Rig Cofor HH300
Drilled in 2014
Duration: 3,5 months

## Slide 30: GRT-2 well testing
GRT-2
High productivity
Low skin
No well development

## Slide 31: GRT-2 Well testing
GRT-1 – GRT-2
Interference test: pressure front in 30mn
Tracer test: breakthrough in 14 days

## Slide 32: Temperature
GRT-1
GRT-2

## Slide 33: Temperature

## Slide 34: Heat delivery loop
15 km between Rittershoffen (drilling site) and Beinheim (bio-refinery)
- 1 natural site (Natura 2000),
- 1 train line,
- 1 motorway,
- 6 primary roads,
- 2 rivers
- 7 gas transport lines
- 1 pipeline

## Slide 35
35
Way back: simple enveloppe
Heat losses 1,5 °C/15 km
Way to: double enveloppe
Heat losses < 4°C/15km
Heat delivery loop

## Slide 36
Heat delivery loop construction

## Slide 37: Heat delivery loop construction

## Slide 38: The heat plant in Rittershoffen
Architect’s views

## Slide 39: The heat plant in Rittershoffen
Real picture

## Slide 40: Experience after 1 year production
Low induced seismicity : 365 induced mEQ detected between April 2016 and march 2017 (max Mlv = 1,4)
GRT-1 injectivity increased drastically

## Slide 41: Lessons learned
Exploration data is extremely important (GRT-1 / GRT-2)
For the wells
  Drill two deviated wells with limited inclination (<35°)
  Use standard casing (20’’ and no 18’’5/8)
At a reservoir scale
  Faults are flow zone in the Rhine Graben
  Convection between to Muschelkalk and weathered granite
  In-fault convection ?
Great injectivity increase of GRT-1 with no fracturation

## Slide 42: Acknowlegements and related publications
Acknowlegements:
  EU project « DESTRESS » (grant agreement No. 691728)
  ADEME Project « EGS ALSACE »
Related Publication
  EGC 2016
    Sosio et al., Integrated Geological, Fluid Flow and Geomechanical Model of a Geothermal Field, Session Exploration T1b
    Hemlich et al., Geodetic measurements for geothermal sites monitoring at Soultz-sous-Forêts and Rittershoffen deep geothermal sites, Session T5b
    Ravier et al., Towards a comprehensive environmental monitoring of a geothermal power plant in the Rhine graben, session T5b
    Maurer et al., Ground vibrations caused by geothermal drilling operations: a case study from the Rittershoffen EGS project (Alsace, France), session T5b
    Vidal et al., Natural fractures and permeability at the geothermal site Rittershoffen, France, Session S6b
    Hehn et al., Stress field rotation in the EGS well GRT-1 (Rittershoffen, France), Session S6b
    + Posters Maurer et al., Richard et al., …
  Stanford 2017, Meyer et al., “Analysis and numerical modelling of pressure drops observed during hydraulic stimulation of GRT-1 geothermal well (Rittershoffen, France)”
  Baujard et al., Geothermics, 2016, “Hydrothermal Characterization of wells GRT-1 and GRT-2 in Rittershoffen, France: Implications on the Understanding of Natural Flow Systems in the Rhine Graben”