## Slide 1: DAP symposium 2019, March 12th
Alexandros Daniilidis, Hamid Nick, David Bruhn
Upscaling Geothermal Heat: Synthetic Models Advising Field Development
Steering committee
Research Funded by:

## Slide 2
Motivation
CO2
<2°C

## Slide 3
Motivation

## Slide 4
Geothermal systems

## Slide 5
Background
Crooijmans et.al. 2016
Three types of reservoir models

## Slide 6
Background
Willems et.al. 2017
Well spacing
Notes: From Willems we know that the lifetime of a systems with facies architecture can be reasonalby captured with a homogeneous model with comparative N/G

## Slide 7
Background
Willems et.al. 2017
Interference – two doublets
Notes: Positive interference for equal well spacing
production rate issues with regards to spacing and pressence of geological features that can alter the pressure field such as a fault
NPV should be looked at for longer than 15 years (beyond subsidy duration)

## Slide 8
Underlying idea
“Simple” synthetic model
Capture uncertainty
Consider scenarios
Obtain generalizable conclusions
Analyze results
“Upscale” findings to field scale
Devise strategy
X1000s realization
Notes: Positive interference for equal well spacing
production rate issues with regards to spacing and pressence of geological features that can alter the pressure field
NPV should be looked at for longer than 15 years (beyond subsidy duration)

## Slide 9
Synthetic model
2 doublets separated by one fault
Notes: Hydraulic Thermal model
Reservoir: 3 layers of 50m, homogeneous flow properties
Over and underburden 250m thickness, really low permeability
Simulate the system for 50 years

## Slide 10
Example simulation
Top view
Notes: Displacement 150m, fault distance center, 800m spacing
Two ways to see this, different operators of west and east doublet, or single operator

## Slide 11
System lifetime
Temperature drop
Notes: East doublet, higher temperature due to increased depth. Pattern similar for all three cases

## Slide 12
System lifetime
Percentage drop T≤95%Tt=0
Notes: Normalizing to initial temperature shows small differences

## Slide 13
NPV
At system lifetime
Notes: Assumes 60euro/MWh price for heat
NPV still positive and increasing but, my main process is not satisfied, beyond the lifetime point
From an NPV perspective we could produce more, if our process could accept lower temperature input.

## Slide 14
System lifetime
Well configuration

## Slide 15
Example simulation
Top view
Uncertainty:
Reservoir layer properties
Fault distance
Fault properties
….
Scenario:
Well spacing
Well arrangement
Flow rate
….
Notes: Displacement 150m, fault distance 200m from West doublet

## Slide 16
System lifetime
Well configurations T ≤ 95% Tt0
Notes: Checherboard configuration always preferable
~20 years of lifetime even at 400m3/hr with 1000m spacing
~20 years of lifetime even at 250m3/hr with 800m spacing

## Slide 17
Systematic Overview
T≤95% Tt0

## Slide 18
Field scale
Notes: Increasing the number of wells, decreasing the well spacing
At field scale with geomodelled flow properties

## Slide 19
Overview
“Simple” synthetic model
Capture uncertainty
Consider scenarios
Obtain generalizable conclusions
Analyze results
“Upscale” findings to field scale
Devise strategy
X1000s realization
Notes: Positive interference for equal well spacing
production rate issues with regards to spacing and pressence of geological features that can alter the pressure field
NPV should be looked at for longer than 15 years (beyond subsidy duration)

## Slide 20
Relevance
Source: Heat Roadmap Europe 2013
Notes: To supply a larger part of the high demand, we need coordinated development of geothermal systems.
A development strategy at the regional scale can signifficantly improve the output per license area and also per finite subsurface space.
Results are already apparent with two doublets and become more relevant as their number increases further.

## Slide 21
Contact:
A.Daniilidis@tudelft.nl